## Slide 1
M.TECH PROJECT PROPOSAL
Deep Reinforcement Learning for
Energy-Optimal Trajectory Planning of UAVs
Under Airspace and Environmental Constraints
Domain: Systems Engineering • Reinforcement Learning • Aerospace
Methods: SAC / DDPG • Point-Mass Dynamics • Optimal Control Baseline

## Slide 2
2
Why This Problem Matters
Fuel is the single largest recurring cost and emissions driver in aerial operations
Energy is finite
UAVs and aircraft operate under strict fuel/battery budgets — every kg of fuel or % of charge shapes mission range and payload.
Manual profiles are suboptimal
Fixed climb-cruise-descent profiles ignore live wind fields and airspace layout, leaving fuel savings on the table.
Constraints are dynamic
No-fly zones, altitude ceilings, and weather change mission-to-mission — static lookup tables can't adapt in real time.
DRL learns adaptive policies
A trained agent can generalize across conditions, replanning trajectories on the fly to balance fuel, time, and safety.

## Slide 3
3
Project Objectives
01
Design an MDP formulation
Define state, action, and reward structure for UAV energy-optimal trajectory planning.
02
Train a continuous-control DRL agent
Use SAC/DDPG to learn climb-cruise-descent policies minimizing fuel/energy use.
03
Enforce operational constraints
Respect no-fly zones, altitude limits, and wind disturbance within the learned policy.
04
Benchmark against classical control
Compare against a dynamic-programming / optimal-control baseline on the same task.
05
Characterize fuel-vs-time trade-offs
Produce Pareto trade-off curves and robustness sweeps for evaluation.

## Slide 4
4
Problem Formulation — MDP Design
Point-mass energy dynamics model as the DRL environment
STATE
Position (x, y), altitude
Velocity, heading
Fuel remaining
Distance to goal
Wind vector (wx, wy)
ACTION
Thrust command
Climb-rate command
Heading-rate command
REWARD
− Fuel burn rate
− Time penalty
− Constraint violation
+ Progress toward goal
Reward: R = −w₁·fuel − w₂·time − w₃·violation − w₄·altitude_dev + w₅·progress

## Slide 5
5
Base Paper Referred
Fuel- and Noise-Minimal Departure Trajectory Using Deep Reinforcement
Learning with Aircraft Dynamics and Topography Constraints
Published in Transportation Engineering (ScienceDirect), 2025
Formulates the aircraft climb-departure trajectory as a DRL problem, optimizing a fuel-and-noise reward under real aircraft dynamics and topography constraints — the same problem structure this project adopts, narrowed to a fuel/energy-only objective with airspace no-fly constraints.
Why this paper anchors the project
Uses DRL (not classical trajectory optimization) for a real flight-dynamics problem
Reward directly penalizes fuel consumption — the core objective of this project
Incorporates operational constraints (topography) analogous to no-fly zones here

## Slide 6
6
Base Paper → Our Increment
What Reference [1] does, and what this project adds on top of it
BASE PAPER [1] — 2025
OUR INCREMENT
Optimizes only the climb / departure phase
Extends to full climb–cruise–descent profile
Joint fuel + noise objective (coupled trade-off)
Isolated fuel/energy-only objective for a cleaner signal
Constrained by topography only
Adds airspace no-fly zones + wind disturbance
Paper-specific aircraft dynamics model
Open-source OpenAP fuel/thrust data in a custom Gym env
No classical baseline reported for comparison
Dynamic-programming baseline built — hard-constraint, zero-violation path (487 kg, verified)
Single-point performance reporting
Fuel-vs-time Pareto frontier + out-of-distribution wind/zone testing
Net increment: single-phase, joint fuel-noise optimization → full-profile, fuel-only, generalization-tested, Pareto-characterized framework — with the environment and DP baseline already implemented and verified.

## Slide 7
7
Problem Statement
Fixed climb-cruise-descent profiles do not adapt to live wind conditions or airspace layout, leaving fuel and energy savings unrealized — while classical re-optimization for every new scenario is computationally expensive for real-time use.
This project asks:
“Can a DRL agent learn a single adaptive policy that plans fuel/energy-optimal climb-cruise-descent trajectories for a UAV, subject to no-fly zones and wind disturbance, that generalizes across conditions without re-solving from scratch?”
Manual/static profiles ignore real-time wind and constraint changes
Classical optimal control is accurate but too slow for on-the-fly replanning
A learned policy could offer near-optimal fuel efficiency with fast inference

## Slide 8
8
Data Source
No labeled dataset is needed for training — data is generated through simulation
OpenAP
Open-source aircraft performance library — provides thrust, drag, and fuel-flow models per aircraft type, used to build a realistic fuel-burn function for the environment.
Simulated Wind Fields
Synthetic wind vectors (constant, gust, or simple stochastic models) generated in-environment to test robustness — no external dataset needed.
Synthetic Airspace Layouts
Procedurally defined no-fly zones and altitude ceilings, randomized across training episodes for generalization.
Self-Generated Rollouts
The DRL agent generates its own training data (state-action-reward trajectories) through repeated simulation episodes — standard for RL.

## Slide 9
9
Feasibility Study
Technical
Mature open-source tools: Gymnasium, Stable-Baselines3, OpenAP
Point-mass model avoids full 6-DOF simulator complexity
SAC/DDPG are well-documented for continuous control
Time (3 months)
Single-agent, single-aircraft scope fits a 12-week plan
No real hardware/flight test dependency
Reduced scope vs. multi-aircraft/ATC problems
Resource
Runs on a single GPU/CPU workstation
No proprietary datasets or licensing required
Small team (1–2 members) sufficient
Verdict: feasible within 3 months with a tightly scoped single-aircraft, static-constraint version of the problem

## Slide 10
10
Tasks Involved — Implementation Steps
01
Environment & dynamics setup
Build custom Gymnasium env with point-mass kinematics + OpenAP-based fuel model
02
Classical baseline
Implement dynamic-programming / optimal-control solver for comparison
03
DRL agent training
Train SAC/DDPG via Stable-Baselines3; iterate on reward shaping
04
Evaluation
Fuel-vs-time Pareto curves, robustness sweeps on unseen wind/zones
05
Reporting
Document results, trajectories, and trade-off analysis

## Slide 11
11
Reference Papers
[1]
Fuel- and noise-minimal departure trajectory using DRL with aircraft dynamics and topography constraints
Transportation Engineering (ScienceDirect), 2025 — Base Paper
[2]
Deep Reinforcement Learning for Trajectory Generation and Optimisation of UAVs
DDPG-based quadcopter trajectory optimization, KU Leuven
[3]
UAV Trajectory Planning in Wireless Sensor Networks for Energy Consumption Minimization by Deep Reinforcement Learning
arXiv:2108.00354
[4]
Energy-Efficient UAV Trajectory Design for Backscatter Communication: A Deep Reinforcement Learning Approach
IEEE Journals & Magazine
[5]
Data Freshness and Energy-Efficient UAV Navigation Optimization: A Deep Reinforcement Learning Approach
IEEE Trans. Intelligent Transportation Systems, 2020

## Slide 12
12
Expected Outcome
A trained SAC/DDPG policy
that generates fuel-efficient climb–cruise–descent trajectories in real time, adapting to wind and static no-fly constraints without re-optimization.
Deliverables:
Trained policy + training curves
Baseline comparison results
Fuel-vs-time Pareto analysis
Final report / thesis chapter
10–20%
Expected fuel savings vs. fixed-profile baseline
Real-time
Policy inference speed vs. re-solved optimal control

## Slide 13
13
System Architecture
Environment
Point-mass dynamics,
wind field, no-fly zones
DRL Agent
SAC / DDPG policy
& value networks
Action
Thrust, climb-rate,
heading-rate
Trajectory
Fuel, time, safety
margin evaluation
Feedback loop: trajectory outcome updates agent policy via reward signal (closed-loop training)
Parallel baseline: Classical optimal-control (DP) solver on the same environment for benchmarking

## Slide 14
14
Tools & Technologies
Simulation
Custom Gymnasium env
Point-mass energy model
Simplified wind field
DRL Framework
Stable-Baselines3
SAC (primary), DDPG
TensorBoard logging
Baseline & Analysis
Dynamic programming solver
NumPy / SciPy
Matplotlib for Pareto plots

## Slide 15
15
Implementation Timeline — 12 Weeks
Wk 1–2
Setup
Environment, dynamics & fuel model
Wk 3–4
Baseline
Classical optimal-control implementation
Wk 5–8
DRL Training
SAC/DDPG training & reward tuning
Wk 9–10
Evaluation
Pareto curves, robustness sweeps
Wk 11–12
Reporting
Writeup & buffer for re-runs

## Slide 16
16
Evaluation Metrics & Expected Outcomes
Evaluation Metrics
Fuel / energy consumption vs. classical baseline
Flight-time vs. fuel Pareto trade-off curve
Robustness to unseen wind & constraint configurations
Constraint-violation rate (no-fly zone incursions)
Training stability (reward convergence curves)
Adaptive
policy generalizes to disturbances
not seen during training
Quantified Trade-off
Clear fuel-vs-time-vs-safety frontier for
mission planners to choose from

## Slide 17
17
Fuel vs. Time Trade-off (Illustrative)
Expected shape of results once evaluation sweeps are complete
Chart: Flight Time (min)
| 70 | 80 | 90 | 100 | 110 | 120
DRL Policy (SAC) | 420 | 360 | 310 | 280 | 260 | 250
Classical Baseline | 470 | 410 | 365 | 335 | 320 | 310

## Slide 18
18
Contribution & Significance
Scalable alternative to classical trajectory optimization
DRL avoids expensive re-solving for every new scenario — inference is fast once trained.
Adaptive, constraint-aware planning
Learned policy generalizes across wind conditions and airspace layouts without re-optimization.
Quantified engineering trade-offs
Explicit fuel-vs-time-vs-safety analysis supports real mission-planning decisions.
Toward intelligent, fuel-aware autonomy for next-generation aerial systems

## Slide 19
Thank You
Questions & Discussion
Deep Reinforcement Learning for Energy-Optimal Trajectory Planning of UAVs